## Slide 1: BlueVoice on Raspberry Pi 3 and Cloud services integration (Amazon AVS and Google Speech-to-text API)

## Slide 2: Application Overview
The ST BVLINK_rbpi3 is the application available for Linux system (eg. Raspberry) that receive the audio exported by a BLE device using the BlueVoice vendor-specific profile. The app allows to use the BLE device like a standard microphone peripheral of the system.
BLE 8-16K Audio transmission
Real Time playback
Capture like standard microphone

## Slide 3: Application architecture
Python 3
Raspberry Pi 3 Model B
BLE
bluez
bluepy
BVLINK_rbpi3
Audio I/O
ALSA (aloop)
sounddevice
HARDWARE
Kernel Space
Python modules
Python application

## Slide 4: System Architecture
ALSA loop device
Headphones
Loudspeakers
ADPCM decoder
ADPCM
8/16KHz
PCM
8/16KHz
BLE
output device
Recording application
e.g. Audacity
Physical output device
ALSA Driver
BlueVoice
Protocol
input device
BVLINK_rbpi3
Raspberry pi 3

## Slide 5: HW and SW requirements
Receiver (Linux platform)
  Raspberry Pi 3 Model B
  Raspbian OS (or compatible)
  Python 3
  BVLINK_rbpi3 application
Transmitter (one of the following)
  FP-AUD-BVLINK1 Function Pack
    SensorTile or BlueCoin or Nucleo+X-Nucleo
  FP-SNS-ALLMEMS1 Function Pack
    SensorTile or BlueCoin or Nucleo+X-Nucleo
  STSW-BLUEMIC-1
    STEVAL-BlueMic-1

## Slide 6: Setup - Transmitter
The chosen firmware must be configured to stream BlueVoice at either 8KHz or 16KHz
  FP-AUD-BVLINK1 or FP-SNS-ALLMEMS1
    BV_ADPCM_Config.sampling_frequency = FR_8000; /* FR_16000; */
    #define AUDIO_IN_SAMPLING_FREQUENCY FR_8000 /* FR_16000 */
  STSW-BLUEMIC-1
    #define AUDIO_SAMPLING_FREQUENCY (uint16_t)(SAMPLING_FREQ_8000) /* SAMPLING_FREQ_16000 */
Connection interval parameter must be set to 8:
  aci_l2cap_connection_parameter_update_request(handle,
  8 /* interval_min*/,
  8 /* interval_max */,
  0 /* slave_latency */,
  400 /*timeout_multiplier*/);

## Slide 7: Install the application
If you start from a clean installation of Raspbian it is recommended to upgrade the system:
  sudo apt-get update
  sudo apt-get upgrade
Download BVLINK_rbpi3 application from github:
  git clone https://github.com/STMicroelectronics-CentralLabs/BlueVoice-for-Linux.git
Run installation scripts (requires root):
  ./installation.sh

## Slide 8: Run the application
Run main.py in BVLINK_rbpi3 directory with the chosen frequency:
  sudo python3 main.py alsa_playback 16000(or 8000) (for real time playback)
  or
  sudo python3 main.py stl_capture 16000(or 8000) (for microphone)
Select the device
Wait connection
New mic peripheral was created
Start audio streaming

## Slide 9: Integration with Amazon AVS

## Slide 10: Install AVS on Raspberry
BVLINK_rbpi3 application can be used in combination with AVS (Alexa Voice Service) using “Alexa avs sample app” for Raspberry.
  Detailed step by step guide is available here: https://github.com/alexa/alexa-avs-sample-app/wiki/Raspberry-Pi
Download and install the Alexa-avs-sample-app
  wget https://github.com/alexa/alexa-avs-sample-app/archive/master.zip
  unzip ./master.zip
  cd alexa-avs-sample-app-master
  ./automated_install.sh
The AVS installation overwrites the “.asoundrc” file in user home directory that needs to be restored manually with one of the templates from BVLINK_rbpi3 directory:
  cp ~/BVLINK_rbpi3/asoundrc_template_8000 ~/.asoundrc
  OR
  cp ~/BVLINK_rbpi3/asoundrc_template_16000 ~/.asoundrc

## Slide 11: Run AVS app
Start web services
  cd ~/Desktop/alexa-avs-sample-app/samples
  cd companionService && npm start
AVS Client
  cd ~/Desktop/alexa-avs-sample-app/samples
  cd javaclient && mvn exec:exec
Wake-up agent
  cd ~/Desktop/alexa-avs-sample-app/samples
  cd wakeWordAgent/src && ./wakeWordAgent -e sensory
Now you can use your transmitter device like a standard microphone to send voice command to AVS

## Slide 12: Speech-to-text using Google API

## Slide 13: Run Speech2Text app
Set up Speech2Text
  ./installation.sh
Set up BVLINK_rbpi3 application as described before
Start BVLINK_rbpi3
  sudo python3 BVLINK_rbpi3 / main.py stl_capture 16000
Start Speech2Text
  python3 Speech2Text_google/main.py
The application waits the speech
Transcribe the speech by Google API and print it

## Slide 14: Chrome browser voice command

## Slide 15: Chrome browser voice command
Start BVLINK_rbpi3 application as described before
Install Hands Free plugin for Chrome
  https://chrome.google.com/webstore/detail/hands-free-for-chrome/ddgmnkioeodkdacpjblmihodjgmebnld
Click on HF button
A new window will be open
Say “help” to get a list of available commands